## Slide 1: IceCube Masterclass Madison, Wisconsin
Jim Haugen
March 7, 2018
IceCube Construction and the South Pole

## Slide 2
Who am I? How did I get here?
- Green Bay East High School grad from a long time ago
- UW grad in Applied Math, Physics and Engineering (’83)
- Back to Madison in 2001 after wafer fab work in Silicon Valley, a startup in MN and IC foundry work in Thailand
- I am the Instrumentation Mgr and South Pole planner for WIPAC, 7 seasons down on the Ice at Pole…
Facilitate the matching of physicist’s ‘dreams’ with an engineer’s ‘reality’

## Slide 3: Briefly, what is IceCube?
This is a federally funded project administered through the National Science Foundation
We completed construction in 2011, started in 2001
We built a Neutrino Telescope (a unique telescope) at the South Pole
Total budget for the project is ~$270M with all US funding managed at the University of Wisconsin
Here is the best part - on time, on budget, on schedule and …..the darn thing works!!!!
http://icecube.wisc.edu/

## Slide 4: IceCube Construction Sequence
Design (2001-2004) Use paper, software and prototypes to design and verify the detector will meet scientific requirements. ‘Freeze’ design before production.
Production (2004-2009) Manufacture (integrate and test) with very high quality all of the materials needed at the Pole. Ship on time!
Logistics (2004-2011) Move millions of pounds of cargo to Pole using trucks, ships, and planes. Many constraints to meet. Everything must fit into a Herc! (slide 33) Get 100 people to the Ice each year.
Installation (2004-2011) Simply, get everything into the Ice (also cabling, IceTop, ICL buildout). Use a giant Hot Water Drill to make holes 2450m deep and deploy the ‘instrumentation strings’.
Commissioning (2005-2011) Make the detector works as expected (fingers were crossed in January, 2005)!!!!

## Slide 5
South Pole 10m Telescope
IceCube Counting Laboratory (ICL)
IceCube Enhanced Hot Water Drill (EHWD)
Drilling site
MAPO (Bicep2)

## Slide 6: IceCube Instrumentation basics
Main items are:
  Digital Optical Module (DOM)
  Surface to DOM cable
  Surface Cable
  IceTop (tanks, DOMs, cables)
  ICL Servers and IT equipment
  Lots of assorted other stuff

## Slide 7
DOMs just before sealing

## Slide 8
IceTop DOMs

## Slide 9
Last one

## Slide 10
Surface cable in Herc

## Slide 11
Start of season

## Slide 12
ICL Cable pull

## Slide 13
Connections in ICL

## Slide 14
Surface to DOM cable arrives at Pole

## Slide 15
Surface to DOM cable on the TU20 getting ready for deployment

## Slide 16
IceTop tanks and Surface Junction Box

## Slide 17: South Pole with IceCube
IceCube
Getting IceCube in the Ice
The Enhanced Hot Water Drill

## Slide 18: Why a Hot Water Drill?
Hot water + Ice = Hole
Fast
Need a water-filled hole
  DOMs freeze in and become optically coupled with ice sheet
  Fluid supports hole so it doesn’t collapse in on itself
  Allows us to circulate water

## Slide 19
DRILL CAMP
HOLE or TOWER SITE
Notes: Note person walking

## Slide 20: How Did It Do?
Chart: Drilling Over Course of Season
2004-2005: 1 (and a half) holes
2009-2010: 20 holes
depth
Notes: 04-05 not actual data, but representative

## Slide 21
Fun South Pole Facts
altitude: ~10,000 ft (9000 + thinner air)
mean temperature in Summer: -31F, -35C
mean temperature in Winter: -80F, -62C
precipitation: 2.5mm/yr (Portland: 922.02/yr)
summer population: 280
winter population: 45
water ration: 2 showers/week, 2 minutes each
sunrises or sunsets per year: 1
distance to McMurdo base: 840 miles / 1355 km
indigenous life: microbes
Antarctica has 90% of the earth’s fresh water locked up in its ice
working at the south pole
Weirdest thing? The sun just spinning around you each day

## Slide 23
~ 40 lbs

## Slide 25
CHC to McM on a C17 out of McChord AFB

## Slide 26
Inside C17

## Slide 29
A not so pretty McMurdo Station

## Slide 31
Finally to Pole…
LC-130 Herc from the 109th ANG wing from New York

## Slide 32
Inside the Herc

## Slide 34
Herc landing at Pole
9.5 million pounds of cargo (fuel and equipment) delivered to Pole in support of IceCube over last 8 seasons…lots of flights!

## Slide 35
Arrival at Pole

## Slide 36
South Pole Station…nice digs
Note absences of penguins…

## Slide 37
Thank You !